## Slide 1
Wind Turbine Failure Detection
MAIN PRESENTATION
Wind Turbine Failure Detection • 01
Aeolus Renewables
Drivetrain condition assessment using 10-minute SCADA measurements
131,760
sensor records
15
turbines
3.00%
recorded faults
Predictive Modeling with Machine Learning and Neural Networks | Low-Code Path
Submission date: October 11, 2026

## Slide 2
Contents / Agenda
MAIN PRESENTATION
Wind Turbine Failure Detection • 02
01
Executive summary and business problem
02
Exploratory analysis and preprocessing
03
Model comparison and final selection
04
Actionable recommendations
A
Appendix: data, baselines, tuning and evidence

## Slide 3
Executive Summary
MAIN PRESENTATION
Wind Turbine Failure Detection • 03
VALIDATION RECALL
92.49%
Tuned ANN selected
TEST RECALL
86.40%
1,245 / 1,441 faults
TEST PRECISION
49.48%
False-alert tradeoff
TEST F1
62.93%
Balance of P and R
The operational decision
Use the ANN as analyst decision support, not an automatic turbine shutdown trigger.
1,271 false-positive records require remote triage; 196 fault records were missed.

## Slide 4
Business Problem Overview and Solution Approach
MAIN PRESENTATION
Wind Turbine Failure Detection • 04
WHY IT MATTERS
Missed drivetrain faults can lead to extended downtime, emergency repairs and lost energy production.
CONDITION-BASED WORKFLOW
01
SCADA readings
→
02
Fault / normal model
→
03
Operations review
→
04
Maintenance action
Method: timestamp-grouped chronological split, training-only preprocessing, five baseline models, two tuned candidates, validation-driven selection.

## Slide 5
EDA Results — Class Balance and Asset Patterns
MAIN PRESENTATION
Wind Turbine Failure Detection • 05
131,760 readings • 15 turbines • 3.00% recorded faults
The minority fault class makes accuracy alone misleading; turbine-level rates support prioritised investigation.

## Slide 6
EDA Results — Sensor Evidence
MAIN PRESENTATION
Wind Turbine Failure Detection • 06
KEY OBSERVATIONS
Vibration, gearbox temperature and oil particles are visibly elevated in fault-state records.
Wind speed alone provides weaker separation, supporting multi-signal evaluation.

## Slide 7
Data Preprocessing and Leakage Prevention
MAIN PRESENTATION
Wind Turbine Failure Detection • 07
DATA QUALITY
0 duplicate rows; missing gearbox-oil (645), generator-bearing (690), oil-pressure (636).
TREATMENT
Training-median imputation; ANN StandardScaler fit using training rows only.
FEATURE ENGINEERING
Time cycles, power utilisation and temperature-rise variables.
EVALUATION DESIGN
Timestamp-grouped chronological 70% / 15% / 15%; test reserved until final evaluation.

## Slide 8
Model Performance Summary and Final Selection
MAIN PRESENTATION
Wind Turbine Failure Detection • 08
Tuned model | Validation recall | F1 | Precision
ANN (selected) | 92.49% | 53.54% | 37.67%
XGBoost | 69.10% | 69.34% | 69.57%
Selection rule
Maximise validation recall; F1 and precision are secondary tie-breakers.
ANN catches more recorded fault states. XGBoost offers better precision and F1, so the false-alert tradeoff must be managed.

## Slide 9
Actionable Business Recommendations
MAIN PRESENTATION
Wind Turbine Failure Detection • 09
01 Triage
Review persistent model alerts and corroborating sensor signals remotely.
02 Dispatch
Prioritise technician inspections when risk persists across successive intervals.
03 Learn
Link alerts to work orders; track false alarms, missed faults, and operational workload.
04 Validate
Run prospective field validation before promising lead time or cost savings.
Evidence base: 196 missed recorded fault states justify recall-first selection; 1,271 false-positive records justify remote triage before a technician visit. Track alert persistence, missed states, false-alert workload, work-order outcomes and data drift during a pilot.

## Slide 10
APPENDIX — Data Background and Contents
APPENDIX
Wind Turbine Failure Detection • 10
SCADA panel
8,784 timestamp groups, recorded at 10-minute intervals across 15 turbines.
Environment
Wind, ambient conditions
Operation
Power and rotational speeds
Condition
Bearing heat, vibration, oil particles
Asset history
Hours, load cycles and maintenance
Target: failure = 1 denotes a recorded fault condition, not a future failure horizon.

## Slide 11
Model Building — Five Baseline Classifiers
APPENDIX
Wind Turbine Failure Detection • 11
Model | Accuracy | Precision | Recall | F1
Decision Tree | 90.70% | 27.74% | 47.93% | 35.14%
Random Forest | 95.35% | 82.87% | 14.44% | 24.59%
Gradient Boosting | 94.54% | 46.96% | 29.74% | 36.42%
XGBoost | 96.64% | 71.01% | 60.83% | 65.53%
ANN | 94.79% | 50.28% | 68.05% | 57.83%
ANN and XGBoost have the highest baseline recall and were selected for tuning.

## Slide 12
Model Improvement — Hyperparameter Tuning
APPENDIX
Wind Turbine Failure Detection • 12
XGBOOST
6 sampled configurations; 2 timestamp-grouped expanding folds; recall objective.
Best CV recall 48.45%; holdout validation recall 69.10%.
ANN
64/24 hidden units; BatchNorm, dropout 0.30/0.15, Adam, early stopping.

## Slide 13
Final Model Performance — Untouched Test
APPENDIX
Wind Turbine Failure Detection • 13
TEST RECALL
86.40%
TEST PRECISION
49.48%
TEST ACCURACY
92.58%
TEST F1
62.93%
1,245 detected • 196 missed
1,271 false alerts • 17,058 true normals

## Slide 14
Feature Interpretation and Limitations
APPENDIX
Wind Turbine Failure Detection • 14
KEY DRIVERS
Drivetrain vibration and oil particle count show the largest validation-recall impacts.
Permutation importance measures association, not causation or a future-failure lead time.

## Slide 15
Timestamp-Grouped Split Verification
APPENDIX
Wind Turbine Failure Detection • 15
TRAIN
92,220
6,148 timestamps
VALIDATION
19,770
1,318 timestamps
TEST
19,770
1,318 timestamps
LEAKAGE CHECK
All 15 turbine records at a timestamp remain in the same partition. Failure prevalence changes over time.

## Slide 16
Operational Use Case and Next Steps
APPENDIX
Wind Turbine Failure Detection • 16
STAGE 1
Model flags current abnormal condition.
STAGE 2
Analyst checks persistence and supporting sensors.
STAGE 3
Maintenance team prioritises planned inspection.
DEPLOYMENT GUARDRAILS
Retrospective proof of concept: prospectively validate alert value, technician workload, model drift and downtime outcomes before automated action or savings claims.

## Slide 17
EDA Results — Multivariate Sensor Relationships
MAIN PRESENTATION • 17
Correlation heatmap uses actual SCADA values across thermal, vibration, oil and operating variables.
What the data shows
• Drivetrain vibration has the strongest positive correlation with recorded fault condition (0.54).
• Oil-particle count is also materially positive (0.47); bearing-frequency vibration is 0.23.
• Oil pressure is negatively related (-0.17); gearbox bearing temperature is weaker (0.10).
Business implication
No single sensor separates every state. The multi-channel model combines complementary signals and reduces dependence on rigid individual thresholds.

## Slide 18
Tuning Comparison — Recall First, Precision Trade-off
APPENDIX • 18
Both candidates were chosen from baseline validation evidence. Selection used holdout validation recall only; test results were excluded.
Model | Baseline P / R / F1 | Tuned P / R / F1 | Tuning method
ANN | 50.28% / 68.05% / 57.83% | 37.67% / 92.49% / 53.54% | 64/24 units; BatchNorm; dropout 0.30/0.15; Adam; early stopping
XGBoost | 71.01% / 60.83% / 65.53% | 69.57% / 69.10% / 69.34% | 6 randomized configurations; two expanding timestamp-grouped folds
Why ANN is selected
ANN has the highest validation recall (92.49%), so it detects more recorded fault states under the declared business priority. XGBoost has higher precision and F1, making it a credible lower-alert-burden alternative. This trade-off is documented rather than hidden.